## Slide 1: Chapter 5
Computing Components

## Slide 2: Chapter Goals (1 of 2)
  Read an ad for a computer and understand the jargon
  List the components and their function in a von Neumann machine
  Describe the fetch-decode-execute cycle of the von Neumann machine
  Describe how computer memory is organized and accessed

## Slide 3: Chapter Goals (2 of 2)
Name and describe different auxiliary storage devices
Define three alternative parallel computer configurations
Explain the concept of embedded systems and give examples from your own home

## Slide 4: Computer Components
Consider the following computer specification:

## Slide 5: Sizes in Perspective (1 of 3)
Admiral Grace Murray Hopper’s illustration
  A coil of wire nearly 1,000 feet long
    Distance traveled by an electron along the wire in the space of a microsecond
  A short piece of wire
    In the space of a nanosecond
  A bag containing grains of pepper
    In the space of a picosecond

## Slide 6: Sizes in Perspective (2 of 3)
Powers of 10 for time, powers of 2 for storage

## Slide 7: Sizes in Perspective (3 of 3)
Intel Processor
Speed 2.66 GHz
SDRAM
Size 4GB
Speed 800 MHz
500GB SATA at 5400 RPM
Transfer rate 300MB per second
Flat screen dot pitch .28mm
To which do these apply?
Bigger is better
Faster is better
Smaller is better

## Slide 8: Stored-Program Concept
Instructions and data are both stored in memory unit
The von Neumann architecture

## Slide 9: Memory (1 of 2)
Memory
A collection of cells, each with a unique physical address
Most computers are byte-addressable
Cell at address 11111110 contains 10101010
“Little endian” bit numbering:

## Slide 10: Memory (2 of 2)
Memory
What does 10101010 mean?
No way to answer that without applying an interpretation.
Could be an instruction, a natural number, a signed integer, a character, part of an image, …

## Slide 11: Arithmetic/Logic Unit
Performs basic arithmetic operations such as addition and subtraction
Performs logical operations such as AND, OR, and NOT
Most modern ALUs have a small amount of special storage units called registers that can be accessed faster than main memory

## Slide 12: Input/Output Units
Input Unit
A device through which data and programs from
the outside world enter the computer system
Can you name three?
Output Unit
A device through which results stored in the
computer memory are made available outside the computer system
Can you name two?

## Slide 13: Control Unit
Control Unit
The organizing force in the computer
Instruction Register (IR)
Contains the instruction that is being executed
Program Counter (PC)
Contains the address of the next instruction to be
executed
Central Processing Unit (CPU)
ALU and the control unit called the Central Processing Unit, or CPU

## Slide 14: Flow of Information
Bus
In general: A communication system that transfers data between components inside a computer or between computers; the medium (wires, optical fiber, etc.) and the protocols (rules for sharing the medium nicely)
“The” bus: Connects the CPU, main memory, I/O devices, and possibly other components (e.g., hard disk drive)
Data flow through a von Neumann machine

## Slide 15: What is an N-bit Processor?
It could mean any of these:
N-bit general registers
N-bit ALU
N-bit addresses
N-bit data bus

## Slide 16: The Fetch-Execute Cycle (1 of 2)
Fetch the next instruction
Decode the instruction
Get data if needed
Execute the instruction
Why is it called a cycle?

## Slide 17: The Fetch-Execute Cycle (2 of 2)
The fetch-execute cycle

## Slide 18: RAM and ROM
Random Access Memory (RAM)
Memory in which each location can be accessed and changed
Read Only Memory (ROM)
Memory in which each location can be accessed but not changed
RAM is volatile, ROM is not.
What does volatile mean?

## Slide 19: Secondary Storage Devices
Why is it necessary to have secondary storage devices?
Can you name some of these devices?

## Slide 20: Magnetic Tape
The first truly mass auxiliary storage device was the magnetic tape drive
Tape drives have a
major problem; can
you describe it?
A magnetic tape

## Slide 21: Magnetic Disks (1 of 2)
The organization of a magnetic disk (A) A single disk
The organization of a magnetic disk (b) A hard disk drive

## Slide 22: Magnetic Disks (2 of 2)
Seek Time
Time for read/write head to be over right track
Latency
Time for sector to be in position
Access Time
Can you define it?
Transfer Rate
Rate at which data moves from the disk to memory

## Slide 23: Optical Disks
CD
A compact disk that uses a laser to read information stored optically on a plastic-coated disk; data is evenly distributed around spiral track
CD-ROM read-only memory
CD-DA digital audio
CD-WORM write once, read many
RW or RAM both read from and written to
DVD
Digital Versatile Disk, used for storing audio and video
Blu-ray
Higher capacity DVD allowing higher resolution video, etc.

## Slide 24: Flash Drives
24
Flash Memory
Nonvolatile
Can be erased and rewritten
Supports USB mass storage standard
Flash drive
© Brian A. Jackson/Shutterstock
Notes: 24

## Slide 25: Touch Screens (1 of 5)
Touch Screen
A computer monitor that can respond to the user touching the screen with a stylus or finger
There are four types
  Resistive
  Capacitive
  Infrared
  Surface acoustic wave (SAW)

## Slide 26: Touch Screens (2 of 5)
Resistive Touch Screen
A screen made up of two layers of electrically conductive material
  One layer has vertical lines, the other has horizontal lines
  When the top layer is pressed, it comes in contact with the second layer, which allows electrical current to flow
  The specific vertical and horizontal lines that make contact dictate the location on the screen that was touched

## Slide 27: Touch Screens (3 of 5)
Capacitive Touch Screen
A screen made up of a laminate applied over a glass screen
  Laminate conducts electricity in all directions; a very small current is applied equally on the four corners
  When the screen is touched, current flows to the finger or stylus
  The location of the touch on the screen is determined by comparing how strong the flow of electricity is from each corner

## Slide 28: Touch Screens (4 of 5)
Infrared Touch Screen
A screen with crisscrossing horizontal and vertical beams of infrared light
  Sensors on opposite sides of the screen detect the beams
  When the user breaks the beams by touching the screen, the location of the break can be determined

## Slide 29: Touch Screens (5 of 5)
Surface Acoustic Wave (SAW)
A screen with criss-crossing high frequency sound waves across the horizontal and vertical axes
  When a finger touches the surface, corresponding sensors detect the interruption and determine location of the touch

## Slide 30: Embedded Systems
30
Embedded Systems
Computers that are dedicated to perform
a narrow range of functions as part of a
larger system
Empty your pockets or backpacks.
How many embedded systems do you have?
Notes: 30

## Slide 31: Parallel Computing
Four general forms:
Bit-level parallelism
  Bits can be processed simultaneously
  Ex: Increasing word size
Instruction-level parallelism
  Instructions can be executed simultaneously
  Ex: Pipelining (overlapping instructions)
  Ex: Superscalar (multiple execution units)
Data-level parallelism
  Data subjected to same operation sequence simultaneously
  Ex: Calculation of all students’ GPAs simultaneously
Task-level parallelism
  Entire tasks can be completed simultaneously
  Ex: Google servers – simultaneous independent searches
  Ex: “Pipelined” processors

## Slide 32: Shared Memory Parallel Processor
Communicate through shared memory
A shared-memory parallel processor

## Slide 33: Ethical Issues
Is Privacy a Thing of the Past?
  What does Austin Bay say about the printing press? The camera? The telegraph? The telephone?
  Do you agree that personal privacy is “all but dead and gone”?
  What, if anything, needs to be done about it?
  What does Bay say about the future of institutional and state secrecy?

## Slide 34: Who Am I?
A lawsuit determined my
legacy.
What was it all about?

## Slide 35: Do You Know?
Maurice Wilkes made what far-reaching discovery within 6 weeks of beginning to program?
What was stolen at Target during the 2013 Christmas shopping season?
Bush received 4,258 votes and Kerry received 260 votes, out of 638 votes cast. How can this discrepancy be explained?
Why have spies infiltrated the fantasy world of virtual games?
What did President Obama refuse to give up?